## Slide 1
Design & Implementation of a Secure Office LAN
-RIP Routing, ACLs, SSH Encryption
COMPUTER NETWORKS
19ECE311

## Slide 2
Project Overview
Network Design
& Topology
Purpose: To create and simulate a secure Local Area Network (LAN) that represents a typical office environment with multiple departments interconnected.
Simulation Tool: Cisco Packet Tracer
Implemented:
RIP v2 (Routing Information Protocol) for dynamic routing.
SSH (Secure Shell) for encrypted remote access.
Password protection at console, VTY, and enable levels.
Access Control Lists (ACLs) for traffic control and internal security.
Topology: A Mesh Topology connecting 3 routers (R0, R1, R2) ensures redundancy and multiple paths for data.
IP Addressing
Scheme
Routing Protocol
-RIP v2

## Slide 3
Project Overview
Network Design
& Topology
Routers: R0, R1, and R2 form a triangle (full mesh) using GigabitEthernet interfaces.
LANs: Each router connects to a separate LAN (e.g., R0 for HR, R1 for Admin, R2 for IT).
Router Connections:
R0 ↔ R1
R1 ↔ R2
R2 ↔ R0
Diagram:
IP Addressing
Scheme
Routing Protocol
-RIP v2
SSH & Device
Security

## Slide 4
Network Design
& Topology
IP Addressing
Scheme
LAN Subnets:
R0 LAN: 192.168.10.0/24
R1 LAN: 192.168.20.0/24
R2 LAN: 192.168.30.0/24
Inter-router Links :
Use /30 subnets to minimize waste:
  R0–R1: 10.0.0.0/30
  R1–R2: 10.0.0.4/30
  R2–R0: 10.0.0.8/30
IP Table: Include a screenshot from CPT showing interface IPs of routers and PCs.
Routing Protocol
-RIP v2
SSH & Device
Security
Project Overview
Password Encryption
Access Control Lists

## Slide 5
IP Addressing
Scheme
Routing Protocol
-RIP v2
Reason for RIP v2:
Easy to configure.
Efficient for small, flat networks.
Supports CIDR (Classless Inter-Domain Routing) and subnetting.
Configuration Steps:
  router rip
  version 2
  network 192.168.10.0
  network 192.168.20.0
  network 192.168.30.0
  network 10.0.0.0
Verification:
Use show ip route to check that RIP has populated the routing table.
Include a screenshot showing RIP routes with “R” next to them.
SSH & Device
Security
Network Design
& Topology
Project Overview
Password Encryption
Access Control Lists
ACL Testing & Results

## Slide 6
Routing Protocol
-RIP v2
SSH Configuration Steps:
Set hostname and domain:
hostname R0
ip domain-name example.com
Create user:
username admin privilege 15 secret admin123
Generate RSA keys:
  crypto key generate rsa
Choose key size: 1024 bits
Configure VTY lines:
line vty 0 4
login local
transport input ssh
Verification: Use PC terminal or PuTTY to SSH into router using IP address.
SSH & Device
Security
Password Encryption
IP Addressing
Scheme
Network Design
& Topology
Project Overview
Access Control Lists
ACL Testing & Results
Additional Features
Considered

## Slide 7
SSH & Device
Security
Password Encryption
Enable Secret:
More secure than plain-text enable password.
Usage:
  enable secret mysecurepassword
Encrypt all passwords:
  service password-encryption
Console Password:
  line console 0
  password myconsolepass
  login
Prevents unauthorized CLI access.
Access Control Lists
Routing Protocol
-RIP v2
IP Addressing
Scheme
Network Design
& Topology
ACL Testing & Results
Additional Features
Considered

## Slide 8
Password Encryption
Goal: Restrict access from R2's LAN (IT) to R1's LAN (Admin).
ACL Configuration:
  access-list 20 deny ip 192.168.30.0 0.0.0.255 192.168.20.0 0.0.0.255 access-list 20 permit ip any any
  interface g0/0
  ip access-group 20 in
Explanation:
  Denies packets from 192.168.30.0/24 to 192.168.20.0/24.
  Allows all other traffic.
Where Applied: On R1’s G0/0 interface (facing LAN).
Access Control Lists
ACL Testing & Results
SSH & Device
Security
Routing Protocol
-RIP v2
Additional Features
Considered
Outcomes &
Learnings
IP Addressing
Scheme

## Slide 9
Password Encryption
Access Control Lists
ACL Testing & Results
SSH & Device
Security
Routing Protocol
-RIP v2
Additional Features
Considered
Outcomes &
Learnings
IP Addressing
Scheme
ACL blocking between R1 and R2
ACL blocking between R2 and R1

## Slide 10
Ping Tests:
  R2 → R1 PC: Blocked
  R0 ↔ R1 / R2: Allowed
Commands Used:
  ping 192.168.20.x from R2 PC (fail)
  ping 192.168.20.x from R0 PC (pass)
Verification:
  show access-lists
This displays hit counts on the ACL rules to confirm the match.
Access Control Lists
ACL Testing & Results
Additional Features
Considered
Password Encryption
SSH & Device
Security
Challenges Faced
Outcomes &
Learnings
Routing Protocol
-RIP v2

## Slide 11
✅ DHCP Snooping – Explored to prevent rogue DHCP servers but not implemented.
✅ Syslog – Helpful for logging events, explored.
✅ Port Security – Can restrict switch ports to specific MACs.
❌ VLANs – Not implemented due to single LAN per router.
❌ GRE VPN – Attempted but caused routing/ACL conflicts, hence excluded.
ACL Testing & Results
Additional Features
Considered
Challenges Faced
Access Control Lists
Password Encryption
Outcomes &
Learnings
SSH & Device
Security

## Slide 12
ACL Matching: Ensuring correct wildcard masks and matching source-destination IPs.
ACL Direction: Confusion over inbound (in) vs outbound (out) interfaces.
SSH Testing: Needed accurate IP, credentials, and port availability.
GRE VPN: Conflicted with ACLs and caused unreachable routes, required rollback.
Additional Features
Considered
Challenges Faced
Outcomes &
Learnings
Access Control Lists
Password Encryption
ACL Testing & Results

## Slide 13
Successfully simulated a secure and functional LAN network.
Understood and implemented:
  Routing protocols
  Secure remote access (SSH)
  Password encryption
  Traffic restriction via ACL
Gained hands-on knowledge of network planning, configuration, and troubleshooting.
Learned layered security techniques in networking (physical, data link, and network layer).
Challenges Faced
Outcomes &
Learnings
Additional Features
Considered
ACL Testing & Results
Access Control Lists

## Slide 14
T
H
A
N
K
Y
O
U